## Slide 1: Part 6 Chapter 24
Boundary-Value Problems
PowerPoints organized by Dr. Michael R. Gustafson II, Duke University
All images copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Chapter Objectives
Understanding the difference between initial-value and boundary-value problems.
Knowing how to express an nth order ODE as a system of n first-order ODEs.
Knowing how to implement the shooting method for linear ODEs by using linear interpolation to generate accurate “shots.”
Understanding how derivative boundary conditions are incorporated into the shooting method.

## Slide 3: Objectives (cont)
Knowing how to solve nonlinear ODEs with the shooting method by using root location to generate accurate “shots.”
Knowing how to implement the finite-difference method.
Understanding how derivative boundary conditions are incorporated into the finite-difference method.
Knowing how to solve nonlinear ODEs with the finite-difference method by using root location methods for systems of nonlinear algebraic equations.

## Slide 4: Boundary-Value Problems
Boundary-value problems are those where conditions are not known at a single point but rather are given at different values of the independent variable.
Boundary conditions may include values for the variable or values for derivatives of the variable.
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 5: Higher Order Systems
MATLAB’s ODE solvers are based on solving first-order differential equations only.
To solve an nth order system (n>1), the system must be written as n first-order equations:
Each first-order equation needs an initial value or boundary value to solve.

## Slide 6: The Shooting Method
One method for solving boundary-value problems - the shooting method - is based on converting the boundary-value problem into an equivalent initial-value problem.
Generally, the equivalent system will not have sufficient initial conditions and so a guess is made for any undefined values.
The guesses are changed until the final solution satisfies all the boundary conditions.
For linear ODEs, only two “shots” are required - the proper initial condition can be obtained as a linear interpolation of the two guesses.
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 7: Boundary Conditions
Dirichlet boundary conditions are those where a fixed value of a variable is known at a particular location.
Neumann boundary conditions are those where a derivative is known at a particular location.
Shooting methods can be used for either kind of boundary condition.

## Slide 8: The Shooting Method for Nonlinear ODEs
For nonlinear ODEs, interpolation between two guesses will not necessarily result in an accurate estimate of the required boundary condition.
Instead, the boundary condition can be used to write a roots problem with the estimate as a variable.

## Slide 9: Example
Solve with ’=2.7x10-9 K-3 m-2, L=10 m, h’=0.05 m-2, T=200 K, T(0) = 300 K, and T(10) = 400 K.
First - break into two equations:

## Slide 10: Example Code
Code for derivatives: function dy=dydxn(x,y) dy=[y(2);… -0.05*(200-y(1))-2.7e-9*(1.6e9-y(1)^4)];
Code for residual: function r=res(za) [x,y]=ode45(@dydxn, [0 10], [300 za]); r=y(length(x),1)-400;
Code for finding root of residual: fzero(@res, -50)
Code for solving system: [x,y]=ode45(@dydxn, [0 10], [300 fzero(@res, -50) ]);

## Slide 11: Finite-Difference Methods
The most common alternatives to the shooting method are finite-difference approaches.
In these techniques, finite differences are substituted for the derivatives in the original equation, transforming a linear differential equation into a set of simultaneous algebraic equations.

## Slide 12: Finite-Difference Example
Convert: into n-1 simultaneous equations at each interior point using centered difference equations:

## Slide 13: Finite-Difference Example (cont)
Since T0 and Tn are known, they will be on the right-hand-side of the linear algebra system (in this case, in the first and last entries, respectively):

## Slide 14: Derivative Boundary Conditions
Neumann boundary conditions are resolved by solving the centered difference equation at the point and rewriting the system equation accordingly.
For example, if there is a Neumann condition at the T0 point,

## Slide 15: Finite-Difference Method for Nonlinear ODEs
Root location methods for systems of equations may be used to solve nonlinear ODEs.
Another method is to adapt a successive substitution algorithm to calculate the values of the interior points.